## Slide 1: MRPL REFINERY OPERATIONS BRIEFING
Crude Distillation Unit (CDU-1) Furnace F-101 Turnaround Plan
Generated by Sovereign Agentic AI Workbench

## Slide 2: Furnace F-101 Overheating Anomaly
• Inspection Finding: Thermocouple TT-104 detected 620°C radiant tube skin temperature.
• SOP-MRPL-FURNACE-01 Violation: Safe operating envelope capped at 610°C (10°C breach).
• Corrosion Measurement: Radiant Zone B localized thinning observed at 0.45 mm/year.
• Immediate Mandatory Action: De-rate firing from 104% to ≤80% MCR within 24 hours.

## Slide 3: 7-Day Decoking Turnaround Milestone Schedule
• Day 1-2: Firing de-rating and crude throughput rebalancing to CDU-2.
• Day 3-4: Unit isolation, steam-air decoking, and pigging of radiant passes.
• Day 5-6: Hydrostatic re-testing, ultrasonic gauge verification, and refractory inspection.
• Day 7: Safe unit start-up and ramp-up under CGM sign-off protocol.